## Slide 1: Router Construction II
Outline
  Network Processors
  Adding Extensions
  Scheduling Cycles

## Slide 2: Observations
Emerging commodity components can be used to build IP routers
  switching fabrics, network processors, …
Routers are being asked to support a growing array of services
  firewalls, proxies, p2p nets, overlays, ...

## Slide 3: Router Architecture
Data Plane
(IP)
Control Plane
(BGP, RSVP…)
Notes: Logical view of router
  Primary job: IP packets IN OUT
Only few packets require extra work
  Or destined for router itself
Separation of traffic reflected in these two components

## Slide 4: Software-Based Router
+ Cost
+ Programmability
– Performance (~300 Kpps)
– Robustness
Data Plane
(IP)
Control Plane
(BGP, RSVP…)
PC
Notes: One approach mapping logical to HW
  PC, single CPU
Couple of advantages
  Originally workstations
  Recent trend: proxies, firewalls, QoS, etc…
Get what you pay for
Difficult to secure against DoS attacks
  Example: control over data OR data over control

## Slide 5: Hardware-Based Router
– Cost
– Programmability
+ Performance (25+ Mpps)
+ Robustness
Data Plane
(IP)
Control Plane
(BGP, RSVP…)
ASIC
PC
Notes: Another approach
Robust
  No bad traffic patterns, all packets at LINE SPEED guaranteed basic processing
Downside
  Hardcode common case packet assumption
  If wrong, same boat as prev slide
Against recent trend  more packets want processing

## Slide 6: NP-Based Router Architecture
+ Cost ($1500)
+ Programmability
? Performance
? Robustness
Data Plane
(packet flows)
Control Plane
(packet flows)
IXP1200
PC
Notes: Leads to our approach
Define Network Processor
Hope for “best of both worlds”
  IXP is processor, you can program
But there are challenges
  The point of the talk
Focus on Data Plane, but don’t forget Control Plane

## Slide 7: In General...
IXP
Pentium
IXP
Pentium
...
Pentium

## Slide 8: Architectural Overview
. . . Network Services . . .
Virtual
Router
. . . Hardware Configurations . . .
Packet Flows
Forwarding Paths
Switching Paths

## Slide 9: Virtual Router
Classifiers
Schedulers
Forwarders

## Slide 10: Simple Example
IP
Proxy
Active Protocol

## Slide 11: Intel IXP
Scratch
DRAM
SRAM
6 Micro-
Engines
StrongARM
FIFOs
IX Bus
MAC Ports
IXP1200 Chip
PCI Bus

## Slide 12: Processor Hierarchy
MicroEngines
Pentium
StrongArm

## Slide 13: Data Plane Pipeline
DRAM
(buffers)
SRAM
(queues,
state)
Input
FIFO Slots
Output
FIFO Slots
Input
Contexts
Output
Contexts
64B
Notes: Graphical overview of static resource assignments

## Slide 14: Data Plane Processing
INPUT context loop
wait_for_data
copy in_fiforegs
Basic_IP_processing
copy regsDRAM
if (last_fragment)
enqueueSRAM
OUTPUT context loop
if (need_data)
select_queue
dequeueSRAM
copy DRAMout_fifo
Notes: IP = validate header, addr cache lookup, TTL, checksum, choose dest queue
  Relate to “basic IP” instr counts

## Slide 15: Pipeline Evaluation
100Mbps Ether  0.142Mpps
Measured independently
Notes: Now look at how fast the processing is
8 + 16 = 24, and all are multiples of 4

## Slide 16: What We Measured
Static context assignment
  16 input / 8 output
Infinite offered load
64-byte (minimum-sized) IP packets
Three different queuing disciplines
Notes: All boils down to problem central to HW fabrics : queuing strategies

## Slide 17: Single Protected Queue
Lock synchronization
Max 3.47 Mpps
Contention lower bound 1.67 Mpps
O
I
I
I
Output FIFO
Notes: One-to-one correspondence of queues and output contexts
Speed bounded by output

## Slide 18: Multiple Private Queues
Output must select queue
Max 3.29 Mpps
O
I
I
I
Output FIFO
Notes: Speed still bounded by output
  Slower because extra output work

## Slide 19: Multiple Protected Queues
Output must select queue
Some QoS scheduling (16 priority levels)
Max 3.29 Mpps
O
I
I
I
Output FIFO
Notes: Most interesting to combine the two
Allows some QoS
  We chose 16 queues per output context
  16 QoS priorities – fairly rich
Speed still bounded by output contexts

## Slide 20: Data Plane Processing
INPUT context loop
wait_for_data
copy in_fiforegs
Basic_IP_processing
copy regsDRAM
if (last_fragment)
enqueueSRAM
OUTPUT context loop
if (need_data)
select_queue
dequeueSRAM
copy DRAMout_fifo
Notes: This is all contexts do
Infinite ports  runs as fast as contexts can go, no waiting
But if not at Princeton and cannot afford infinite ports…
  Your contexts block on wait_for_data

## Slide 21: Cycles to Waste
INPUT context loop
wait_for_data
copy in_fiforegs
Basic_IP_processing
nop
nop
…
nop
copy regsDRAM
if (last_fragment)
enqueueSRAM
OUTPUT context loop
if (need_data)
select_queue
dequeueSRAM
copy DRAMout_fifo
Notes: Instead of blocking on wait_for_data
  Add extra instructions
  Pace context to packet rate

## Slide 22: How Many “NOPs” Possible?
IXP1200 Evalualtion Board
1.2 Mpps = 8x100Mbps
Notes: Graph shows
  For different packet rates
  Extra instr budget, what fits in loop
Example to explain graph

## Slide 23: Data Plane Extensions

## Slide 24: Control and Data Plane
Smart Dropper
Layered Video Analysis
(control plane)
(data plane)
Shared State

## Slide 25: What About the StrongARM?
Shares memory bus with MicroEngines
  must respect resource budget
What we do
  control IXP1200  Pentium DMA
  control MicroEngines
What might be possible
  anything within budget
  exploit instruction and data caches
We recommend against
  running Linux
Notes: DMA is within resource budget

## Slide 26: Performance
MicroEngines
Pentium
StrongArm
310Kpps with
1510 cycles/packet
3.47Mpps w/ no VRP
or
1.13Mpps w/ VRP buget

## Slide 27: Pentium
Runs protocols in the control plane
  e.g., BGP, OSPF, RSVP
Run other router extensions
  e.g., proxies, active protocols, overlays
Implementation
  runs Scout OS + Linux IXP driver
  CPU scheduler is key

## Slide 28: Processes
.
.
.
.
.
.
.
.
.
.
.
.
Input Port
Pentium
Output Port
P
P
P
P
P

## Slide 29: Performance

## Slide 30: Performance (cont)
Kpps

## Slide 31: Scheduling Mechanism
Proportional share forms the base
  each process reserves a cycle rate
  provides isolation between processes
  unused capacity fairly distributed
Eligibility
  a process receives its share only when its source queue is not empty and sink queue is not full
Batching
  to minimize context switch overhead
Notes: use PS to meet these goals
PS: static
elig: complementary mechanism , dynamic
because we introduced a pipeline, producer/consumer
relationship, can not always perfectly accurate
e.g, if share all smaller, queue full, go to sleep
shares goes to consumer

## Slide 32: Share Assignment
QoS Flows
  assume link rate is given, derive cycle rate
  conservative rate to input process
  keep batching level low
Best Effort Flows
  may be influenced by admin policy
  use shares to balance system (avoid livelock)
  keep batching level high
Notes: more specifically
need to set the process shares along the pipeline
assume some knowledge of forwarding cost

## Slide 33: Experiment
A (BE)
B (QoS)
C (QoS)
A + C
B

## Slide 34: Mixing Best Effort and QoS
Increase offered load from A
Notes: what we wanna see:
for qos, can we make our commitement
be, good use of resources

## Slide 35: CPU vs Link
Fix A at 50Kpps, increase its processing cost
Notes: last example is link bound wanna study cpu
simulate cpu hog
batching became the killer
at a time, only very fewer process is eligible

## Slide 36: Turn Batching Off
CPU efficiency: 66.2%
Notes: cycles used to forwarding packets as oppose to
csw and polling empty interfaces

## Slide 37: Enforce Time Slice
CPU efficiency: 81.6% (30us quantum)
Notes: can handle varying workload well
tradeoff between performance and properties

## Slide 38: Batching Throttle
Scheduler Granularity: G
  flow processes as many packets as possible w/in G
Efficiency Index: E, Overhead Threshold: T
  keep the overhead under T%, then 1 / (1+T) < E
Batch Threshold: Bi
  don’t consider Flow i active until it has accumulated at least Bi packets, where Csw / (Bi x Ci) < T
Delay Threshold: Di
  consider a flow that has waited Di active
Notes: Bi: the batch number depends on the processing cost of the flow
goal is: when schedule a flow with at least bi backlog, the csw that
followed will add no more than t% overhead
Di for latency sensitive flows time out scheme

## Slide 39: Dynamic Control
Flow specifies delay requirement D
Measure context switch overhead offline
Record average flow runtime
Set E based on workload
Calculate batch-level B for flow

## Slide 40: Packet Trace