## Slide 1: Internetworking
Outline
  Best Effort Service Model
  Global Addressing Scheme

## Slide 2: IP Internet
Concatenation of Networks
Protocol Stack

## Slide 3: Service Model
Connectionless (datagram-based)
Best-effort delivery (unreliable service)
  packets are lost
  packets are delivered out of order
  duplicate copies of a packet are delivered
  packets can be delayed for a long time
Datagram format

## Slide 4: Fragmentation and Reassembly
Each network has some MTU
Design decisions
  fragment when necessary (MTU < Datagram)
  try to avoid fragmentation at source host
  re-fragmentation is possible
  fragments are self-contained datagrams
  use CS-PDU (not cells) for ATM
  delay reassembly until destination host
  do not recover from lost fragments

## Slide 5: Example
(a)
Ident = x
Start of header
Rest of header
1400 data bytes
Offset = 0
0
(b)
Ident = x
Start of header
Rest of header
512 data bytes
Offset = 0
1
Ident = x
Rest of header
512 data bytes
Offset = 64
1
Start of header
Ident = x
Start of header
Rest of header
376 data bytes
Offset = 128
0

## Slide 6: Global Addresses
Properties
  globally unique
  hierarchical: network + host
Dot Notation
  10.3.2.4
  128.96.33.81
  192.12.69.77

## Slide 7: Datagram Forwarding
Strategy
  every datagram contains destination’s address
  if connected to destination network, then forward to host
  if not directly connected, then forward to some router
  forwarding table maps network number into next hop
  each host has a default router
  each router maintains a forwarding table
Example (R2) Network Number Next Hop
1 R3
2 R1
3 interface 1
4 interface 0

## Slide 8: Address Translation
Map IP addresses into physical addresses
  destination host
  next hop router
Techniques
  encode physical address in host part of IP address
  table-based
ARP
  table of IP to physical address bindings
  broadcast request if IP address not in table
  target machine responds with its physical address
  table entries are discarded if not refreshed

## Slide 9: ARP Details
Request Format
  HardwareType: type of physical network (e.g., Ethernet)
  ProtocolType: type of higher layer protocol (e.g., IP)
  HLEN & PLEN: length of physical and protocol addresses
  Operation: request or response
  Source/Target-Physical/Protocol addresses
Notes
  table entries timeout in about 10 minutes
  update table with source when you are the target
  update table if already have an entry
  do not refresh table entries upon reference

## Slide 10: ARP Packet Format
TargetHardwareAddr (bytes 2
5)
TargetProtocolAddr (bytes 0
3)
SourceProtocolAddr (bytes 2
3)
Hardware type = 1
ProtocolType = 0x0800
SourceHardwareAddr (bytes 4
5)
TargetHardwareAddr (bytes 0
1)
SourceProtocolAddr (bytes 0
1)
HLen = 48
PLen = 32
Operation
SourceHardwareAddr (bytes 0
―
3)
0
8
16
31
―
―
―
―
―
―

## Slide 11: Internet Control Message Protocol (ICMP)
Echo (ping)
Redirect (from router to source host)
Destination unreachable (protocol, port, or host)
TTL exceeded (so datagrams don’t cycle forever)
Checksum failed
Reassembly failed
Cannot fragment