## Slide 1: Router Construction
Outline
  Switched Fabrics
  IP Routers
  Tag Switching

## Slide 2: Workstation-Based
Aggregate bandwidth
  1/2 of the I/O bus bandwidth
  capacity shared among all hosts connected to switch
  example: 1Gbps bus can support 5 x 100Mbps ports (in theory)
Packets-per-second
  must be able to switch small packets
  300,000 packets-per-second is achievable
  e.g., 64-byte packets implies 155Mbps

## Slide 3: Switching Hardware
Design Goals
  throughput (depends on traffic model)
  scalability (a function of n)
Ports
  circuit management (e.g., map VCIs, route datagrams)
  buffering (input and/or output)
Fabric
  as simple as possible
  sometimes do buffering (internal)
Switch
fabric
Control
processor
Output
port
Input
port

## Slide 4: Buffering
Wherever contention is possible
  input port (contend for fabric)
  internal (contend for output port)
  output port (contend for link)
Head-of-Line Blocking
  input buffering

## Slide 5: Crossbar Switches

## Slide 6: Knockout Switch
Example crossbar
Concentrator
  select l of n packets
Complexity: n2
1
2
3
4
Outputs
Inputs

## Slide 7: Knockout Switch (cont)
Output Buffer
(c)
Shifter
Buffers
(b)
Shifter
Buffers
(a)
Shifter
Buffers

## Slide 8: Self-Routing Fabrics
Banyan Network
  constructed from simple 2 x 2 switching elements
  self-routing header attached to each packet
  elements arranged to route based on this header
  no collisions if input packets sorted into ascending order
  complexity: n log2 n

## Slide 9: Self-Routing Fabrics (cont)
Batcher Network
  switching elements sort two numbers
    some elements sort into ascending (clear)
    some elements sort into descending (shaded)
  elements arranged to implement merge sort
  complexity: n log22 n
Common Design: Batcher-Banyan Switch

## Slide 10: High-Speed IP Router
Switch (possibly ATM)
Line Cards
  link interface (input, output)
  router lookup (input)
  common IP path (input)
  packet queue (output)
Control Processor
  routing protocol(s)
  exceptional cases
Line card
(forwarding
buffering)
Line card
(forwarding
buffering)
Line card
(forwarding
buffering)
Line card
(forwarding
buffering)
Routing
CPU
Buffer
memory
Routing software
w/ router OS

## Slide 11: IP Forwarding is Slow
Problem: classless IP addresses (CIDR)
Route by variable-length Forwarding Equivalence Classes (FEC)
  FEC = IP address plus prefix of 1-32 bits; e.g., 172.200.0.0/16
IP Router
  forwarding tbl: <FEC> <next hop, port>
  match IP address to FEC w/ longest prefix

## Slide 12: ATM Forwarding
Primary goal: fast, cheap forwarding
1Gb/s IP router: $187,000
5Gb/s ATM switch: $41,000
Create Virtual Circuit at Flow Setup
  <in VCI> <port, out VCI>
Cell Forwarding
  index, swap, switch

## Slide 13: Cisco: Tag Switching
Add a VCI-like tag to packets
  <in tag> <next hop, port, out tag>
TSR uses ATM switch hardware
IP routing protocols (OSPF, RIP, BGP)
  build forwarding table from routing table
Goal: IP router functionality at ATM switch speeds/costs

## Slide 14: Forwarding
Shim before IP header
Tag Forwarding Information Base (TFIB)
  <in tag> <next hop, port, out tag>
Just like ATM
  index, swap, switch
TTL (8 bits)
CoS
S
Tag (20 bits)

## Slide 15: Tag Binding
New FEC from IP routing protocols
  Select local tag (index in TFIB)
  <in tag> <next hop, port, ???>
Need <out tag> for next hop
Other routers need my <in tag>
Solution: distribute tags like other routing info

## Slide 16: Tag Distribution Protocol
Send TDP messages to peers
  <FEC, my tag>
Upon receiving TDP message, check if sender is next hop for FEC
  yes, save tag in TFIB
  no, can discard or save for future use
‘Control-driven’ label assignment

## Slide 17: The First Tag
Two kinds of routers: edge vs. interior
Edge: add shim based on IP lookup, strip at exit
Interior: forward by tag only
E
I
I
E

## Slide 18: Robustness Issues
What if tag fault?
  try to forward (default route)
  discard packet
Forwarding Loops
  topology changes cause temporary loops
  TTL field in tag, same as IP

## Slide 19: Ipsilon: IP Switching
Run on ATM switch over ATM network
  ATM hardware + IP switching software
Idea: Exploit temporal locality of traffic to cache routing decisions
Associate labels (VCI) with flows
  forward packets as usual
  main difference is in how labels are created, distributed to other routers

## Slide 20: IP Switch
Assume default ATM virtual circuits between routers
Router runs IP routing protocol, can forward IP packets on default VCs
Identify flows, assign flow-specific VC
  flow = port pair or host pair
‘Data-driven’ label assignment

## Slide 21: Flow Setup on IP Switch
<vci = x> <port c, vci = x’>
Get IFMP, <vci = x> <port j, vci = y>
ATM Switch
Controller
Port i
Port j
vci = x
vci = y
<flowID, vci = x, life>
<flowID, vci = y, life>
Port c
vci = x’
IFMP message
IFMP message

## Slide 22: Comparison
Switch by flow
Data driven
Soft-state timeout
Between end-hosts
Every router can do IP lookup
Scalable?
Switch by FEC
Control driven
Route changes
Between edge TSRs
Interior TSRs only do tag switching
IP Switching
Tag Switching