## Slide 1: Multimedia
Outline
  Compression
  RTP
  Scheduling

## Slide 2: Compression Overview
Encoding and Compression
  Huffman codes
Lossless
  data received = data sent
  used for executables, text files, numeric data
Lossy
  data received does not != data sent
  used for images, video, audio

## Slide 3: Lossless Algorithms
Run Length Encoding (RLE)
  example: AAABBCDDDD encoding as 3A2B1C4D
  good for scanned text (8-to-1 compression ratio)
  can increase size for data with variation (e.g., some images)
Differential Pulse Code Modulation (DPCM)
  example AAABBCDDDD encoding as A0001123333
  change reference symbol if delta becomes too large
  works better than RLE for many digital images (1.5-to-1)

## Slide 4: Dictionary-Based Methods
Build dictionary of common terms
  variable length strings
Transmit index into dictionary for each term
Lempel-Ziv (LZ) is the best-known example
Commonly achieve 2-to-1 ration on text
Variation of LZ used to compress GIF images
  first reduce 24-bit color to 8-bit color
  treat common sequence of pixels as terms in dictionary
  not uncommon to achieve 10-to-1 compression (x3)

## Slide 5: Image Compression
JPEG: Joint Photographic Expert Group (ISO/ITU)
Lossy still-image compression
Three phase process
  process in 8x8 block chunks (macro-block)
  grayscale: each pixel is three values (YUV)
  DCT: transforms signal from spatial domain into and equivalent signal in the frequency domain (loss-less)
  apply a quantization to the results (lossy)
  RLE-like encoding (loss-less)

## Slide 6: Quantization and Encoding
Quantization Table
3 5 7 9 11 13 15 17
5 7 9 11 13 15 17 19
7 9 11 13 15 17 19 21
9 11 13 15 17 19 21 23
11 13 15 17 19 21 23 25
13 15 17 19 21 23 25 27
15 17 19 21 23 25 27 29
17 19 21 23 25 27 29 31
Encoding Pattern

## Slide 7: MPEG
Motion Picture Expert Group
Lossy compression of video
First approximation: JPEG on each frame
Also remove inter-frame redundancy

## Slide 8: MPEG (cont)
Frame types
  I frames: intrapicture
  P frames: predicted picture
  B frames: bidirectional predicted picture
Example sequence transmitted as I P B B I B B

## Slide 9: MPEG (cont)
B and P frames
  coordinate for the macroblock in the frame
  motion vector relative to previous reference frame (B, P)
  motion vector relative to subsequent reference frame (B)
  delta for each pixel in the macro block
Effectiveness
  typically 90-to-1
  as high as 150-to-1
  30-to-1 for I frames
  P and B frames get another 3 to 5x

## Slide 10: MP3
CD Quality
  44.1 kHz sampling rate
  2 x 44.1 x 1000 x 16 = 1.41 Mbps
  49/16 x 1.41 Mbps = 4.32 Mbps
Strategy
  split into some number of frequency bands
  divide each subband into a sequence of blocks
  encode each block using DCT + Quantization + Huffman
  trick: how many bits assigned to each subband

## Slide 11: RTP
Application-Level Framing
Data Packets
  sequence number
  timestamp (app defines “tick”)
Control Packets (send periodically)
  loss rate (fraction of packets received since last report)
  measured jitter

## Slide 12: Transmitting MPEG
Adapt the encoding
  resolution
  frame rate
  quantization table
  GOP mix
Packetization
Dealing with loss
GOP-induced latency

## Slide 13: Layered Video
Layered encodeing
  e.g., wavelet encoded
Receiver Layered Multicast (RLM)
  transmit each layer to a different group address
  receivers subscribe to the groups they can “afford”
  Probe to learn if you can afford next higher group/layer
Smart Packet Dropper (multicast or unicast)
  select layers to send/drop based on observed congestion
  observe directly or use RTP feedback

## Slide 14: Real-Time Scheduling
Priority
Earliest Deadline First (EDF)
Rate Monotonic (RM)
Proportional Share
  with feedback
  with adjustments for deadlines