## Slide 1: Quality of Service
Outline
  Realtime Applications
  Integrated Services
  Differentiated Services

## Slide 2: Realtime Applications
Require “deliver on time” assurances
  must come from inside the network
Example application (audio)
  sample voice once every 125us
  each sample has a playback time
  packets experience variable delay in network
  add constant factor to playback time: playback point
Microphone
Speaker
Sampler,
A D
converter
Buffer,
D A

## Slide 3: Playback Buffer
Sequence number
Packet
generation
Network
delay
Buffer
Playback
T
ime
Packet
arrival

## Slide 4: Example Distribution of Delays

## Slide 5: Taxonomy

## Slide 6: Integrated Services
Service Classes
  guaranteed
  controlled-load
Mechanisms
  signalling protocol
  admission control
  policing
  packet scheduling

## Slide 7: Flowspec
Rspec: describes service requested from network
  controlled-load: none
  guaranteed: delay target
Tspec: describes flow’s traffic characteristics
  average bandwidth + burstiness: token bucket filter
  token rate r
  bucket depth B
  must have a token to send a byte
  must have n tokens to send n bytes
  start with no tokens
  accumulate tokens at rate of r per second
  can accumulate no more than B tokens

## Slide 8: Per-Router Mechanisms
Admission Control
  decide if a new flow can be supported
  answer depends on service class
  not the same as policing
Packet Processing
  classification: associate each packet with the appropriate reservation
  scheduling: manage queues so each packet receives the requested service

## Slide 9: Reservation Protocol
Called signaling in ATM
Proposed Internet standard: RSVP
Consistent with robustness of today’s connectionless model
Uses soft state (refresh periodically)
Designed to support multicast
Receiver-oriented
Two messages: PATH and RESV
Source transmits PATH messages every 30 seconds
Destination responds with RESV message
Merge requirements in case of multicast
Can specify number of speakers

## Slide 10: RSVP Example
Sender 1
Sender 2
PATH
PATH
RESV
(merged)
RESV
RESV
Receiver B
Receiver A
R
R
R
R
R

## Slide 11: RSVP versus ATM (Q.2931)
RSVP
  receiver generates reservation
  soft state (refresh/timeout)
  separate from route establishment
  QoS can change dynamically
  receiver heterogeneity
ATM
  sender generates connection request
  hard state (explicit delete)
  concurrent with route establishment
  QoS is static for life of connection
  uniform QoS to all receivers

## Slide 12: Differentiated Services
Problem with IntServ: scalability
Idea: segregate packets into a small number of classes
  e.g., premium vs best-effort
Packets marked according to class at edge of network
Core routers implement some per-hop-behavior (PHB)
Example: Expedited Forwarding (EF)
  rate-limit EF packets at the edges
  PHB implemented with class-based priority queues or WFQ

## Slide 13: DiffServ (cont)
Assured Forwarding (AF)
  customers sign service agreements with ISPs
  edge routers mark packets as being “in” or “out” of profile
  core routers run RIO: RED with in/out