## Slide 1: Introduction
Outline
  Statistical Multiplexing
  Inter-Process Communication
  Network Architecture
  Performance Metrics
  Implementation Issues

## Slide 2: Building Blocks
Nodes: PC, special-purpose hardware…
  hosts
  switches
Links: coax cable, optical fiber…
  point-to-point
  multiple access
■ ■ ■
(a)
(b)

## Slide 3: Switched Networks
  two or more nodes connected by a link, or
  two or more networks connected by a node
A network can be defined recursively as...

## Slide 4: Strategies
Circuit switching: carry bit streams
  original telephone network
Packet switching: store-and-forward messages
  Internet

## Slide 5: Addressing and Routing
Address: byte-string that identifies a node
  usually unique
Routing: process of forwarding messages to the destination node based on its address
Types of addresses
  unicast: node-specific
  broadcast: all nodes on the network
  multicast: some subset of nodes on the network

## Slide 6: Multiplexing
Time-Division Multiplexing (TDM)
Frequency-Division Multiplexing (FDM)

## Slide 7: Statistical Multiplexing
On-demand time-division
Schedule link on a per-packet basis
Packets from different sources interleaved on link
Buffer packets that are contending for the link
Buffer (queue) overflow is called congestion
■ ■ ■

## Slide 8: Inter-Process Communication
Turn host-to-host connectivity into process-to-process communication.
Fill gap between what applications expect and what the underlying technology provides.

## Slide 9: IPC Abstractions
Request/Reply
  distributed file systems
  digital libraries (web)
Stream-Based
  video: sequence of frames
    1/4 NTSC = 352x240 pixels
    (352 x 240 x 24)/8=247.5KB
    30 fps = 7500KBps = 60Mbps
  video applications
    on-demand video
    video conferencing

## Slide 10: What Goes Wrong in the Network?
Bit-level errors (electrical interference)
Packet-level errors (congestion)
Link and node failures
Packets are delayed
Packets are deliver out-of-order
Third parties eavesdrop

## Slide 11: Layering
Use abstractions to hide complexity
Abstraction naturally lead to layering
Alternative abstractions at each layer

## Slide 12: Protocols
Building blocks of a network architecture
Each protocol object has two different interfaces
  service interface: operations on this protocol
  peer-to-peer interface: messages exchanged with peer
Term “protocol” is overloaded
  specification of peer-to-peer interface
  module that implements this interface

## Slide 13: Interfaces

## Slide 14: Protocol Machinery
Protocol Graph
  most peer-to-peer communication is indirect
  peer-to-peer is direct only at hardware level
Host 1
Host 2
File
application
Digital
library
application
Video
application
File
application
Digital
library
application
Video
application

## Slide 15: Machinery (cont)
Multiplexing and Demultiplexing (demux key)
Encapsulation (header/body)
Host
Host
Application
program
Application
program
RRP
Data
Data
HHP
RRP
HHP
Application
program
Application
program
RRP Data
RRP Data
HHP RRP Data

## Slide 16: Internet Architecture
Defined by Internet Engineering Task Force (IETF)
Hourglass Design
Application vs Application Protocol (FTP, HTTP)
■ ■ ■
FTP
TCP
UDP
IP
NET
1
NET
2
NET
n
HTTP
NV
TFTP

## Slide 17: ISO Architecture

## Slide 18: Performance Metrics
Bandwidth (throughput)
  data transmitted per time unit
  link versus end-to-end
  notation
    KB = 210 bytes
    Mbps = 106 bits per second
Latency (delay)
  time to send message from point A to point B
  one-way versus round-trip time (RTT)
  components
    Latency = Propagation + Transmit + Queue
    Propagation = Distance / c
    Transmit = Size / Bandwidth

## Slide 19: Bandwidth versus Latency
Relative importance
  1-byte: 1ms vs 100ms dominates 1Mbps vs 100Mbps
  25MB: 1Mbps vs 100Mbps dominates 1ms vs 100ms
Infinite bandwidth
  RTT dominates
    Throughput = TransferSize / TransferTime
    TransferTime = RTT + 1/Bandwidth x TransferSize
  1-MB file to 1-Gbps link as 1-KB packet to 1-Mbps link

## Slide 20: Delay x Bandwidth Product
Amount of data “in flight” or “in the pipe”
Usually relative to RTT
Example: 100ms x 45Mbps = 560KB

## Slide 21: Socket API
Creating a socket
  int socket(int domain, int type, int protocol)
    domain = PF_INET, PF_UNIX
    type = SOCK_STREAM, SOCK_DGRAM, SOCK_RAW
Passive Open (on server)
  int bind(int socket, struct sockaddr *addr, int addr_len)
  int listen(int socket, int backlog)
  int accept(int socket, struct sockaddr *addr, int addr_len)

## Slide 22: Sockets (cont)
Active Open (on client)
  int connect(int socket, struct sockaddr *addr,
  int addr_len)
Sending/Receiving Messages
  int send(int socket, char *msg, int mlen, int flags)
  int recv(int socket, char *buf, int blen, int flags)

## Slide 23: Protocol-to-Protocol Interface
Configure multiple layers
  static versus extensible
Process Model
  avoid context switches
Buffer Model
  avoid data copies