## Slide 1: Congestion Control
Outline
  Queuing Discipline
  Reacting to Congestion
  Avoiding Congestion

## Slide 2: Issues
Two sides of the same coin
  pre-allocate resources so at to avoid congestion
  control congestion if (and when) is occurs
Two points of implementation
  hosts at the edges of the network (transport protocol)
  routers inside the network (queuing discipline)
Underlying service model
  best-effort (assume for now)
  multiple qualities of service (later)
Destination
1.5-Mbps T1 link
Router
Source
2
Source
1
100-Mbps FDDI
10-Mbps Ethernet

## Slide 3: Framework
Connectionless flows
  sequence of packets sent between source/destination pair
  maintain soft state at the routers
Taxonomy
  router-centric versus host-centric
  reservation-based versus feedback-based
  window-based versus rate-based
Router
Source
2
Source
1
Source
3
Router
Router
Destination
2
Destination
1

## Slide 4: Evaluation
Fairness
Power (ratio of throughput to delay)
Optimal
load
Load
Throughput/delay

## Slide 5: Queuing Discipline
First-In-First-Out (FIFO)
  does not discriminate between traffic sources
Fair Queuing (FQ)
  explicitly segregates traffic based on flows
  ensures no flow captures more than its share of capacity
  variation: weighted fair queuing (WFQ)
Problem?
Flow 1
Flow 2
Flow 3
Flow 4
Round-robin
service

## Slide 6: FQ Algorithm
Suppose clock ticks each time a bit is transmitted
Let Pi denote the length of packet i
Let Si denote the time when start to transmit packet i
Let Fi denote the time when finish transmitting packet i
Fi = Si + Pi
When does router start transmitting packet i?
  if before router finished packet i - 1 from this flow, then immediately after last bit of i - 1 (Fi-1)
  if no current packets for this flow, then start transmitting when arrives (call this Ai)
Thus: Fi = MAX (Fi - 1, Ai) + Pi

## Slide 7: FQ Algorithm (cont)
For multiple flows
  calculate Fi for each packet that arrives on each flow
  treat all Fi’s as timestamps
  next packet to transmit is one with lowest timestamp
Not perfect: can’t preempt current packet
Example
Flow 1
Flow 2
(a)
(b)
Output
Output
F = 8
F = 10
F = 5
F = 10
F = 2
Flow 1
(arriving)
Flow 2
(transmitting)

## Slide 8: TCP Congestion Control
Idea
  assumes best-effort network (FIFO or FQ routers)each source determines network capacity for itself
  uses implicit feedback
  ACKs pace transmission (self-clocking)
Challenge
  determining the available capacity in the first place
  adjusting to changes in the available capacity

## Slide 9: Additive Increase/Multiplicative Decrease
Objective: adjust to changes in the available capacity
New state variable per connection: CongestionWindow
  limits how much data source has in transit
  MaxWin = MIN(CongestionWindow, AdvertisedWindow)
  EffWin = MaxWin - (LastByteSent - LastByteAcked)
Idea:
  increase CongestionWindow when congestion goes down
  decrease CongestionWindow when congestion goes up

## Slide 10: AIMD (cont)
Question: how does the source determine whether or not the network is congested?
Answer: a timeout occurs
  timeout signals that a packet was lost
  packets are seldom lost due to transmission error
  lost packet implies congestion

## Slide 11: AIMD (cont)
In practice: increment a little for each ACK
Increment = (MSS * MSS)/CongestionWindow
CongestionWindow += Increment
Source
Destination
…
Algorithm
  increment CongestionWindow by one packet per RTT (linear increase)
  divide CongestionWindow by two whenever a timeout occurs (multiplicative decrease)

## Slide 12: AIMD (cont)
Trace: sawtooth behavior
60
20
1.0
2.0
3.0
4.0
5.0
6.0
7.0
8.0
9.0
KB
T
ime (seconds)
70
30
40
50
10
10.0

## Slide 13: Slow Start
Objective: determine the available capacity in the first
Idea:
  begin with CongestionWindow = 1 packet
  double CongestionWindow each RTT (increment by 1 packet for each ACK)
Source
Destination
…

## Slide 14: Slow Start (cont)
Exponential growth, but slower than all at once
Used…
  when first starting connection
  when connection goes dead waiting for timeout
Trace
Problem: lose up to half a CongestionWindow’s worth of data
60
20
1.0
2.0
3.0
4.0
5.0
6.0
7.0
8.0
9.0
KB
70
30
40
50
10

## Slide 15: Fast Retransmit and Fast Recovery
Problem: coarse-grain TCP timeouts lead to idle periods
Fast retransmit: use duplicate ACKs to trigger retransmission
Packet 1
Packet 2
Packet 3
Packet 4
Packet 5
Packet 6
Retransmit
packet 3
ACK 1
ACK 2
ACK 2
ACK 2
ACK 6
ACK 2
Sender
Receiver

## Slide 16: Results
Fast recovery
  skip the slow start phase
  go directly to half the last successful CongestionWindow (ssthresh)
60
20
1.0
2.0
3.0
4.0
5.0
6.0
7.0
KB
70
30
40
50
10

## Slide 17: Congestion Avoidance
TCP’s strategy
  control congestion once it happens
  repeatedly increase load in an effort to find the point at which congestion occurs, and then back off
Alternative strategy
  predict when congestion is about to happen
  reduce rate before packets start being discarded
  call this congestion avoidance, instead of congestion control
Two possibilities
  router-centric: DECbit and RED Gateways
  host-centric: TCP Vegas

## Slide 18: DECbit
Add binary congestion but to each packet header
Router
  monitors average queue length over last busy+idle cycle
  set congestion bit if average queue length > 1
  attempts to balance throughout against delay
Queue length
Current
time
T
ime
Current
cycle
Previous
cycle
A
veraging
interval

## Slide 19: End Hosts
Destination echoes bit back to source
Source records how many packets resulted in set bit
If less than 50% of last window’s worth had bit set
  increase CongestionWindow by 1 packet
If 50% or more of last window’s worth had bit set
  decrease CongestionWindow by 0.875 times

## Slide 20: Random Early Detection (RED)
Notification is implicit
  just drop the packet (TCP will timeout)
  could make explicit by marking the packet
Early random drop
  rather than wait for queue to become full, drop each arriving packet with some drop probability whenever the queue length exceeds some drop level

## Slide 21: RED Details
Compute average queue length
  AvgLen = (1 - Weight) * AvgLen +
  Weight * SampleLen
    0 < Weight < 1 (usually 0.002)
    SampleLen is queue length each time a packet arrives
MaxThreshold
MinThreshold
A
vgLen

## Slide 22: RED Details (cont)
Two queue length thresholds
  if AvgLen <= MinThreshold then
  enqueue the packet
  if MinThreshold < AvgLen < MaxThreshold then
  calculate probability P
  drop arriving packet with probability P
  if ManThreshold <= AvgLen then
  drop arriving packet

## Slide 23: RED Details (cont)
Computing probability P
    TempP = MaxP * (AvgLen - MinThreshold)/ (MaxThreshold - MinThreshold)
    P = TempP/(1 - count * TempP)
Drop Probability Curve
P(drop)
1.0
MaxP
MinThresh
MaxThresh
A
vgLen

## Slide 24: Tuning RED
Probability of dropping a particular flow’s packet(s) is roughly proportional to the share of the bandwidth that flow is currently getting
MaxP is typically set to 0.02, meaning that when the average queue size is halfway between the two thresholds, the gateway drops roughly one out of 50 packets.
If traffic id bursty, then MinThreshold should be sufficiently large to allow link utilization to be maintained at an acceptably high level
Difference between two thresholds should be larger than the typical increase in the calculated average queue length in one RTT; setting MaxThreshold to twice MinThreshold is reasonable for traffic on today’s Internet
Penalty Box for Offenders

## Slide 25: TCP Vegas
Idea: source watches for some sign that router’s queue is building up and congestion will happen too; e.g.,
  RTT grows
  sending rate flattens

## Slide 26: Algorithm
Let BaseRTT be the minimum of all measured RTTs (commonly the RTT of the first packet)
If not overflowing the connection, then
ExpectRate = CongestionWindow/BaseRTT
Source calculates sending rate (ActualRate) once per RTT
Source compares ActualRate with ExpectRate
Diff = ExpectedRate - ActualRate
if Diff < 
increase CongestionWindow linearly
else if Diff > 
decrease CongestionWindow linearly
else
leave CongestionWindow unchanged

## Slide 27: Algorithm (cont)
Parameters
   = 1 packet
   = 3 packets
Even faster retransmit
  keep fine-grained timestamps for each packet
  check for timeout on first duplicate ACK