## Slide 1
Outline
  Encoding
  Framing
  Error Detection
  Sliding Window Algorithm
Point-to-Point Links

## Slide 2: Encoding
Signals propagate over a physical medium
  modulate electromagnetic waves
  e.g., vary voltage
Encode binary data onto signals
  e.g., 0 as low signal and 1 as high signal
  known as Non-Return to zero (NRZ)
Bits
NRZ
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0

## Slide 3: Problem: Consecutive 1s or 0s
Low signal (0) may be interpreted as no signal
High signal (1) leads to baseline wander
Unable to recover clock

## Slide 4: Alternative Encodings
Non-return to Zero Inverted (NRZI)
  make a transition from current signal to encode a one; stay at current signal to encode a zero
  solves the problem of consecutive ones
Manchester
  transmit XOR of the NRZ encoded data and the clock
  only 50% efficient.

## Slide 5: Encodings (cont)
4B/5B
  every 4 bits of data encoded in a 5-bit code
  5-bit codes selected to have no more than one leading 0 and no more than two trailing 0s
  thus, never get more than three consecutive 0s
  resulting 5-bit codes are transmitted using NRZI
  achieves 80% efficiency

## Slide 6: Encodings (cont)
Bits
NRZ
Clock
Manchester
NRZI
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0

## Slide 7: Framing
Break sequence of bits into a frame
Typically implemented by network adaptor
Frames
Bits
Adaptor
Adaptor
Node B
Node A

## Slide 8: Approaches
Sentinel-based
  delineate frame with special pattern: 01111110
  e.g., HDLC, SDLC, PPP
  problem: special pattern appears in the payload
  solution: bit stuffing
    sender: insert 0 after five consecutive 1s
    receiver: delete 0 that follows five consecutive 1s
Header
Body
8
16
16
8
CRC
Beginning
sequence
Ending
sequence

## Slide 9: Approaches (cont)
Couter-based
  include payload length in header
  e.g., DDCMP
  problem: count field corrupted
  solution: catch when CRC fails

## Slide 10: Approaches (cont)
Clock-based
  each frame is 125us long
  e.g., SONET: Synchronous Optical Network
  STS-n (STS-1 = 51.84 Mbps)

## Slide 11: Cyclic Redundancy Check
Add k bits of redundant data to an n-bit message
  want k << n
  e.g., k = 32 and n = 12,000 (1500 bytes)
Represent n-bit message as n-1 degree polynomial
  e.g., MSG=10011010 as M(x) = x7 + x4 + x3 + x1
Let k be the degree of some divisor polynomial
  e.g., C(x) = x3 + x2 + 1

## Slide 12: CRC (cont)
Transmit polynomial P(x) that is evenly divisible by C(x)
  shift left k bits, i.e., M(x)xk
  subtract remainder of M(x)xk / C(x) from M(x)xk
Receiver polynomial P(x) + E(x)
  E(x) = 0 implies no errors
Divide (P(x) + E(x)) by C(x); remainder zero if:
  E(x) was zero (no error), or
  E(x) is exactly divisible by C(x)

## Slide 13: Selecting C(x)
All single-bit errors, as long as the xk and x0 terms have non-zero coefficients.
All double-bit errors, as long as C(x) contains a factor with at least three terms
Any odd number of errors, as long as C(x) contains the factor (x + 1)
Any ‘burst’ error (i.e., sequence of consecutive error bits) for which the length of the burst is less than k bits.
Most burst errors of larger than k bits can also be detected
See Table 2.6 on page 102 for common C(x)

## Slide 14: Internet Checksum Algorithm
View message as a sequence of 16-bit integers; sum using 16-bit ones-complement arithmetic; take ones-complement of the result.
u_short
cksum(u_short *buf, int count)
{
register u_long sum = 0;
while (count--)
{
sum += *buf++;
if (sum & 0xFFFF0000)
{
/* carry occurred, so wrap around */
sum &= 0xFFFF;
sum++;
}
}
return ~(sum & 0xFFFF);
}

## Slide 15: Acknowledgements & Timeouts

## Slide 16: Stop-and-Wait
Problem: keeping the pipe full
Example
  1.5Mbps link x 45ms RTT = 67.5Kb (8KB)
  1KB frames imples 1/8th link utilization
Sender
Receiver

## Slide 17: Sliding Window
Allow multiple outstanding (un-ACKed) frames
Upper bound on un-ACKed frames, called window
Sender
Receiver
T
ime
…
…

## Slide 18: SW: Sender
Assign sequence number to each frame (SeqNum)
Maintain three state variables:
  send window size (SWS)
  last acknowledgment received (LAR)
  last frame sent (LFS)
Maintain invariant: LFS - LAR <= SWS
Advance LAR when ACK arrives
Buffer up to SWS frames

SWS
LAR
LFS
…
…

## Slide 19: SW: Receiver
Maintain three state variables
  receive window size (RWS)
  largest frame acceptable (LFA)
  last frame received (NFE)
Maintain invariant: LFA - LFR <= RWS
Frame SeqNum arrives:
  if LFR < SeqNum < = LFA accept
  if SeqNum < = LFR or SeqNum > LFA discarded
Send cumulative ACKs

RWS
NFE
LFA
…
…

## Slide 20: Sequence Number Space
SeqNum field is finite; sequence numbers wrap around
Sequence number space must be larger then number of outstanding frames
SWS <= MaxSeqNum-1 is not sufficient
  suppose 3-bit SeqNum field (0..7)
  SWS=RWS=7
  sender transmit frames 0..6
  arrive successfully, but ACKs lost
  sender retransmits 0..6
  receiver expecting 7, 0..5, but receives second incarnation of 0..5
SWS < (MaxSeqNum+1)/2 is correct rule
Intuitively, SeqNum “slides” between two halves of sequence number space

## Slide 21: Concurrent Logical Channels
Multiplex 8 logical channels over a single link
Run stop-and-wait on each logical channel
Maintain three state bits per channel
  channel busy
  current sequence number out
  next sequence number in
Header: 3-bit channel num, 1-bit sequence num
  4-bits total
  same as sliding window protocol
Separates reliability from order