## Slide 1: Introduction
Outline
  Statistical Multiplexing
  Inter-Process Communication
  Network Architecture
  Performance Metrics

## Slide 2: Building Blocks
Nodes: PC, special-purpose hardware…
  hosts
  switches
Links: coax cable, optical fiber…
  point-to-point
  multiple access
…

## Slide 3: Switched Networks
  two or more nodes connected by a link, or
  two or more networks connected by two or more nodes
A network can be defined recursively as...

## Slide 4: Strategies
Circuit switching: carry bit streams
  original telephone network
Packet switching: store-and-forward messages
  Internet

## Slide 5: Addressing and Routing
Address: byte-string that identifies a node
  usually unique
Routing: process of forwarding messages to the destination node based on its address
Types of addresses
  unicast: node-specific
  broadcast: all nodes on the network
  multicast: some subset of nodes on the network

## Slide 6: Multiplexing
Time-Division Multiplexing (TDM)
Frequency-Division Multiplexing (FDM)
L1
L2
L3
R1
R2
R3
Switch 1
Switch 2

## Slide 7: Statistical Multiplexing
On-demand time-division
Schedule link on a per-packet basis
Packets from different sources interleaved on link
Buffer packets that are contending for the link
Buffer (queue) overflow is called congestion
…

## Slide 8: Inter-Process Communication
Turn host-to-host connectivity into process-to-process communication.
Fill gap between what applications expect and what the underlying technology provides.
Host
Host
Application
Host
Application
Host
Host
Channel

## Slide 9: IPC Abstractions
Request/Reply
  distributed file systems
  digital libraries (web)
Stream-Based
  video: sequence of frames
    1/4 NTSC = 352x240 pixels
    (352 x 240 x 24)/8=247.5KB
    30 fps = 7500KBps = 60Mbps
  video applications
    on-demand video
    video conferencing

## Slide 10: What Goes Wrong in the Network?
Bit-level errors (electrical interference)
Packet-level errors (congestion)
Link and node failures
Messages are delayed
Messages are deliver out-of-order
Third parties eavesdrop

## Slide 11: Layering
Use abstractions to hide complexity
Abstraction naturally lead to layering
Alternative abstractions at each layer
Request/reply
channel
Message stream
channel
Application programs
Hardware
Host-to-host connectivity

## Slide 12: Protocols
Building blocks of a network architecture
Each protocol object has two different interfaces
  service interface: operations on this protocol
  peer-to-peer interface: messages exchanged with peer
Term “protocol” is overloaded
  specification of peer-to-peer interface
  module that implements this interface

## Slide 13: Interfaces
Host 1
Protocol
Host 2
Protocol
High-level
object
High-level
object
Service
interface
Peer-to-peer
interface

## Slide 14: Protocol Machinery
Protocol Graph
  most peer-to-peer communication is indirect
  peer-to-peer is direct only at hardware level
File
application
Digital
library
application
Video
application
RRP
MSP
HHP
Host 1
File
application
Digital
library
application
Video
application
RRP
MSP
HHP
Host 2

## Slide 15: Machinery (cont)
Multiplexing and Demultiplexing (demux key)
Encapsulation (header/body)
RRP
Data
HHP
Application
program
Application
program
Host 1
Host 2
Data
RRP
RRP
Data
HHP
Data
RRP
RRP
Data
HHP

## Slide 16: Internet Architecture
Defined by Internet Engineering Task Force (IETF)
Hourglass Design
Application vs Application Protocol (FTP, HTTP)
…
FTP
HTTP
NV
TFTP
TCP
UDP
IP
NET
1
NET
2
NET
n

## Slide 17: ISO Architecture
Application
Presentation
Session
Transport
End host
One or more nodes
within the network
Network
Data link
Physical
Network
Data link
Physical
Network
Data link
Physical
Application
Presentation
Session
Transport
End host
Network
Data link
Physical

## Slide 18: Performance Metrics
Bandwidth (throughput)
  data transmitted per time unit
  link versus end-to-end
  notation
    KB = 210 bytes
    Mbps = 106 bits per second
Latency (delay)
  time to send message from point A to point B
  one-way versus round-trip time (RTT)
  components
    Latency = Propagation + Transmit + Queue
    Propagation = Distance / c
    Transmit = Size / Bandwidth

## Slide 19: Bandwidth versus Latency
Relative importance
  1-byte: 1ms vs 100ms dominates 1Mbps vs 100Mbps
  25MB: 1Mbps vs 100Mbps dominates 1ms vs 100ms
Infinite bandwidth
  RTT dominates
    Throughput = TransferSize / TransferTime
    TransferTime = RTT + 1/Bandwidth x TransferSize
  1-MB file to 1-Gbps link as 1-KB packet to 1-Mbps link

## Slide 20: Delay x Bandwidth Product
Amount of data “in flight” or “in the pipe”
Example: 100ms x 45Mbps = 560KB